## Slide 1: Linux Kernel Training. Lecture 3
Working with sources. Cross compilation.
First Kernel module.
Oleksandr Redchuk
<oleksandr.redchuk@gmail.com>
March 30, 2020. GlobalLogic

## Slide 2: Linux Kernel Code Style
Not only spaces, braces and indentation… But them also matter.
Consider:
6) Functions (EXPORT_SYMBOL)
7) Centralized exiting of functions (gotos are very useful in some cases)
12) Macros, Enums and RTL (C macros are widely used but be careful)
15) The inline disease (inline not always as good as it might seem)
17) Don't re-invent the kernel macros
20) Conditional Compilation

## Slide 3: Sections handling in build tools and kernel
.text
.data
.init.text
.exit.text
__init, __initdata, __exit, __exitdata, …
mod_main.o
. . .
.text
.data
.init.text
.exit.text
mod_util.o
. . .
+
=
.text (main) .text (util)
.data (main) .data (util)
.init.text (main) .init.text (util)
.exit.text (main) .exit.text (util)
mod.ko
. . .
.init.* section could be removed from memory just after initialization
.exit.* section will not occupy caches until we use it

## Slide 4: Kbuild: the Linux Kernel Build System
Kbuild is infrastructure for building Linux Kernel image, modules and more
There are four major components/concepts it is based on
  Config symbols concept. It is compilation options that is used to select code to compile via C preprocessor conditionals. Good examples are CONFIG_SMP, CONFIG_MODULES, etc.
  Kconfig files. Used to define config symbols, their type, default value, dependencies between each other, summary name and description. It is used to produce correct kernel configurations as well as give hints to the user during configure process.
  .config file. Complete configuration file for platform, containing all config symbols. Should never be modified manually due to config symbol dependencies described by Kconfig.
  Makefiles. This is normal GNU Makefiles containing target definitions, their dependencies etc. It is actually recipe on how to build/perform something from/with kernel sources (e.g. build image).

## Slide 5: Kbuild: config symbols
Have form CONFIG_<name>(_MODULE)?, where <name> is the name of symbol in Kconfig.
  _MODULE suffix is optional and it is present only when kernel configured to support modules (i.e. CONFIG_MODULES) and given config symbol represents that object will be build as module (e.g CONFIG_EXT4_MODULE)
Stored in .config file for later use by scripts/kconfig tools to generate
  <build_dir>/include/config/auto.conf file to be included from Makefiles where they used to conditionally branch code.
  <build_dir>/include/generated/autoconf.h file to be included from <src_dir>/include/linux/kconfig.h, which is included later by <src_dir>/include/asm-generic/export.h and <src_dir>/include/linux/export.h. This is used by C preprocessor to conditionally branch code to build to aid customization at source code level.

## Slide 6: Kbuild: config symbols (cont.)
In Makefiles we can test for config symbols from config/auto.conf using ifdef/ifndef
but the most common way config symbols are used as (will look in depth later)
# somewhere in lib/Makefile
ifdef CONFIG_FUNCTION_TRACER
ORIG_CFLAGS := $(KBUILD_CFLAGS)
KBUILD_CFLAGS = $(subst $(CC_FLAGS_FTRACE),,$(ORIG_CFLAGS))
endif
# somewhere in drivers/net/ethernet/intel/igb/Makefile
obj-$(CONFIG_IGB) += igb.o
igb-objs := igb_main.o igb_ethtool.o e1000_82575.o

## Slide 7: Kbuild: config symbols (cont.)
In C source we can test for config symbols from generated/autoconf.h using standard C preprocessor #ifdef, #ifndef and #if
/*
* Reflects a new waiter being added to the waitqueue.
*/
static inline void hb_waiters_inc(struct futex_hash_bucket *hb)
{
#ifdef CONFIG_SMP
atomic_inc(&hb->waiters);
/*
* Full barrier (A), see the ordering comment above.
*/
smp_mb__after_atomic();
#endif
}

## Slide 8: Kbuild: config symbols (cont.)
Note that to test for module being enabled for build we need something
or , on relatively recent kernels we can use helper C preprocessor macros
#if defined(CONFIG_MYMOD) || defined(CONFIG_MYMOD_MODULE)
/* Do something really nasty here */
#endif
#if IS_ENABLED(CONFIG_MYMOD)
/* Do something useful here. For example call function from MYMOD */
#endif

## Slide 9: Kbuild: config symbols (cont.)
Inside function it is often more usable to use these macro as condition In if() statement. During a constant folding optimization pass the compiler will optimize the if() statement body away or compile it without runtime overhead.
...
if (IS_ENABLED(CONFIG_SOMEOPT)) {
do_some_action();
}
...

## Slide 10: Kbuild: config symbols (cont.)
There are bit more useful helper macros in <linux/kconfig.h> to be used in C source code to test if certain config symbol is “on”
  IS_BUILTIN(CONFIG_FOO) - evaluates to 1 if CONFIG_FOO is set to 'y' in .config, 0 otherwise
  IS_MODULE(CONFIG_FOO) - evaluates to 1 if CONFIG_FOO is set to 'm' in .config, 0 otherwise
  IS_REACHABLE(CONFIG_FOO) - evaluates to 1 if the currently compiled code can call a function defined in code compiled based on CONFIG_FOO
  IS_ENABLED(CONFIG_FOO) - evaluates to 1 if CONFIG_FOO is set to 'y' or 'm', 0 otherwise
Refer to <src_dir>/include/linux/kconfig.h file for more information on how this implemented.

## Slide 11: Kbuild: Kconfig files
These files are plain text files with quite simple syntax, intended to be parsed by scripts/kconfig, which uses bison/flex to implement parser.
They define config symbols (without CONFIG_ prefix) together with their dependencies and metadata.
Dependencies are used to automatically select other config symbols required for configured one. For example CONFIG_NO_HZ_FULL depends on CONFIG_SMP.
Metadata is used by various configuration facilities to produce user friendly, interactive output. We will look at them next.

## Slide 12: Kbuild: Kconfig files (cont.)
Typical Kconfig file have following view
There is “config” symbol ZONE_DMA and metadata
Refer to Documentation/kbuild/kconfig-language.txt for syntax details
config ZONE_DMA
bool "DMA memory allocation support" if EXPERT
default y
help
DMA memory allocation support allows devices with less than 32-bit
addressing to allocate within the first 16MB of address space.
Disable if no such devices will be used.
If unsure, say Y.

## Slide 13: Kbuild: .config file
Ready configuration file with all options, including selected by dependency
It can be edited manually with extra care if you really known that are doing
It’s contents differ between Linux Kernel versions and generally it is not recommended to reuse .config from previous kernel. We will cover right approach later.
Here is head of typical .config file
#
# Automatically generated file; DO NOT EDIT.
# Linux/arm 4.9.20 Kernel Configuration
#
CONFIG_ARM=y
CONFIG_ARM_HAS_SG_CHAIN=y
CONFIG_MIGHT_HAVE_PCI=y
CONFIG_SYS_SUPPORTS_APM_EMULATION=y

## Slide 14: Kbuild: Makefiles
They are regular GNU Makefiles with excellent syntax. There are two names for them currently supported
  Ordinary Makefile with kbuild syntax. Most of in-tree components use this naming
  Kbuild file with same syntax. This is useful for out-of-tree (external) modules development to provide both Linux Kernel Kbuild instructions as well as regular GNU Make targets. This naming is preferred.
Well documented to show what’s they do
It is an entry point for most aspects of Linux Kernel configuration and building
There is number of environment variables they accept to change files location, pass additional flags to the compilers, linkers, etc.

## Slide 15: Kbuild: Makefiles (cont.)
Kbuild syntax of Makefiles is quite simple and convenient. Most of directives specify what and how to build without any extra details.
All implementation details are hidden in core Makefiles implementation in <src_dir>/Makefile, <src_dir>/Kbuild, general Makefiles in <src_dir>/scripts/Makefile* and <src_dir>/arch/$ARCH/ specific makefiles.
Simplest kbuild style makefile might look as following
# Makefile for the Intel(R) PRO/1000 ethernet driver
obj-$(CONFIG_E1000) += e1000.o
e1000-objs := e1000_main.o e1000_hw.o e1000_ethtool.o e1000_param.o

## Slide 16: Kbuild: Makefiles (cont.)
There are lot of predefined kbuild variables. Here is most useful
  obj-y
  obj-m
  asflags-y
  ccflags-y
  cppflags-y
  ldflags-y
We will cover some of them while preparing our first kernel module.
Refer to Documentation/kbuild/makefiles.txt for more information on kbuild makefile syntax and other details.

## Slide 17: Make: entry for Linux Kernel maintenance
Type make help to get detailed help for supported targets and options.
Architecture specific options output of make help depends on ARCH variable: we will talk about it later during cross compilation.
It is good idea to output build results in directory out of the sources directory using O=... option to make
Also it might be useful to see verbose output for actual command used to compile given file. There is many verbose levels supported V=0..2
$ make <target> O=~/kernel/build
$ make <target> V=1

## Slide 18: Make: entry for Linux Kernel maintenance (cont.)
There is another interesting options to make
  C=1..2 is used to pass C source files through semantics preprocessor. By default sparse(1) is used. There are couple of places within kernel where additional, not specific to gcc nor it’s preprocessor attributes are used making code misunderstoods. This includes, but not limited specific types (e.g. __be32, __be16, etc), qualifiers like __user, __kernel, __rcu, __percpu, etc. All of them take effect only when used with semantics preprocessor like sparse(1) and replaced with empty defines overwise. Refer to Documentation/dev-tools/sparse.txt, include/linux/compiler.h file and sparse(1) man page for more information.
  W=1..3 enable compiler extra warnings. More level is set more warnings being added. Refer to scripts/Makefile.extrawarn for more information on warnings being added. It should be noted that exact set of warnings being generated, including ones enabled by default when no `W’ option is given, purely depends on version and capabilities of the compiler. It is recommended to use latest stable version of compiler to get most from this option.

## Slide 19: Make: generic configure targets
There are various ways to configure Linux Kernel
  Interactive
    Using ncurses based terminal user interface (tui). Called with make menuconfig.
    Using command line interface (cli) on terminal. Called with make config.
    Using graphical interfaces based on Qt/GTK+ frameworks. Called with make {x,g}config.
  Non-interactive
    Using existing .config via make oldconfig.
    Using default values via make all{no,yes,mod,def}config
    Using defconfig from ARCH supplied variable via make defconfig.
    Using silentoldconfig/olddefconfig via make {silentoldconfig,olddefconfig}
Also it is possible to save configuration as default via make savedefconfig

## Slide 20: Make: cleanup source tree
If you build kernel in-tree (i.e. without option O=... to make) and want to clean up it there are two possibilities to do that
  Use make mrproper to remove all generated files (e.g. object files .o), configuration and some backup files
  Use make distclean that performs exactly same as make mrproper plus editor backup (e.g. ones ending with ~) and patch files.
If you want to keep information, like config files, required to build external kernel modules, but remove most of generated files not required for that purpose you can use make clean.

## Slide 21: Linux Kernel cross compilation
Allows to build kernel on host system for target.
  It is common that building host and target has different architectures (e.g. building host is x86_64 and target is ARM)
  Often cross compilation if much faster that building directly on target.
  Cross tools are build for building host architecture, while producing result for target.
Building Linux Kernel for architecture other than current host
  Requires to set ARCH environment variable to one of names in arch/
  Requires cross compilation tools prefix specified with CROSS_COMPILE environment variable

## Slide 22: Writing Your First Linux Kernel Module
As usual, when we doing something at first time we trying to make it as simple as possible and writing “Hello, world!” code best fits for this case.
While kernel module which just prints something to message ring buffer is simplest, we need to create kbuild style makefile for this purpose and have kernel headers ready to build modules.
Let’s start with exact kernel module code and write makefile later.

## Slide 23: Writing Your First Linux Kernel Module (cont.)
#include <linux/init.h>
#include <linux/module.h>
#include <linux/printk.h>
MODULE_AUTHOR(“Serhii Popovych <serhii.popovych@globallogic.com”);
MODULE_DESCRIPTION(“Hello, world in Linux Kernel Training”);
MODULE_LICENSE(“Dual BSD/GPL”);
static int __init hello_init(void)
{
printk(KERN_EMERG “Hello, world!\n”);
return 0;
}
static void __exit hello_exit(void)
{
/* Do nothing here right now */
}
module_init(hello_init);
module_exit(hello_exit);

## Slide 24: Writing Your First Linux Kernel Module (cont.)
Let’s look at this module closer
  At first lines we include <linux/init.h>, <linux/module.h> and <linux/printk.h> header files from Linux Kernel tree. First is used to provide __init/__exit macros, second to provide MODULE_*() and module_init()/module_exit() macros, third - to provide printk() function prototype as well as KERN_EMERG define. KERN_EMERG is the highest logging severity.
  Next, hello_init() is called during the module initialization. Usually some static data is initialized here, allocated some dynamic data or performed other actions. In our case we just print string “Hello, world!”. Note that return negative errno value (e.g. -EINVAL) from this function causes module init to fail and prevent module loading.
  Next, hello_exit() called at module unload time it can not fail, so there is no return value is accepted here.

## Slide 25: Writing Your First Linux Kernel Module (cont.)
Now it’s time to create Makefile and build our module
It is good practice to create generic makefile that allows user to build your external kernel module using simple call to make or make <target>. However we known that Linux Kernel uses kbuild style makefiles, which isn’t the same as plain Makefiles to be executed by make directly.
In short, there are three of approaches to write Kbuild makefile for external kernel modules.
  Shared. Single makefile with both Kbuild and generic make parts.
  Separate. Linux Kernel build part stored in Kbuild. Generic make in Makefile.
  Compatible. Both Kbuild and Makefile present and Makefile includes Kbuild.

## Slide 26: Writing Your First Linux Kernel Module (cont.)
Shared. Single makefile with both Kbuild and generic make parts.
Note that <tab> should be inserted before $(MAKE) -C ....
ifneq ($(KERNELRELEASE),)
# kbuild part of makefile
obj-m := hello.o
else
# normal makefile
KDIR ?= /lib/modules/`uname -r`/build
default:
$(MAKE) -C $(KDIR) M=$$PWD
clean:
$(MAKE) -C $(KDIR) M=$$PWD clean
endif

## Slide 27: Writing Your First Linux Kernel Module (cont.)
Separate. Linux Kernel build part stored in Kbuild. Generic make in Makefile.
Kbuild
Makefile
# kbuild part of makefile
obj-m := hello.o
# normal makefile
KDIR ?= /lib/modules/`uname -r`/build
default:
$(MAKE) -C $(KDIR) M=$$PWD
clean:
$(MAKE) -C $(KDIR) M=$$PWD clean

## Slide 28: Writing Your First Linux Kernel Module (cont.)
Compatible. Both Kbuild and Makefile present and Makefile includes Kbuild.
Kbuild
Makefile
# kbuild part of makefile
obj-m := hello.o
ifneq ($(KERNELRELEASE),)
include Kbuild
else
# normal makefile
KDIR ?= /lib/modules/`uname -r`/build
default:
$(MAKE) -C $(KDIR) M=$$PWD
clean:
$(MAKE) -C $(KDIR) M=$$PWD clean
endif

## Slide 29: Writing Your First Linux Kernel Module (cont.)
Regardless of which style of makefile you choose produced results would be the same.
Now it’s time to build your kernel module
If everything is goes well you will get hello.ko, unstripped, ready to use kernel module.
All that most of the rules applied to in-tree kernel modules applied to external modules too.
Refer to Documentation/kbuild/modules.txt for more information.
$ make KDIR=~/kernel/build
# To cleanup after build
$ make KDIR=~/kernel/build clean

## Slide 30: Load your kernel module
Use loopback mount as we did previously to put userspace program too rootfs to put module. Do not forget to unmount loopback after you finish.
Start QEMU for ARM64.
Now use insmod(1) to load your kernel module on target
Note that first message about tainted kernel is normal when loading out-of-tree modules.
root@qemuarm:~# insmod ~/hello.ko
[ 20.885098] hello: loading out-of-tree module taints kernel.
[ 20.898232] Hello, world!

## Slide 31: Looking for module information
When module is loaded we can get certain information about it from kernel procfs and sysfs
root@qemuarm:~# cat /proc/modules
hello 846 0 - Live 0xbf000000 (O)
root@qemuarm:~# cat /proc/sys/kernel/tainted
4096
root@qemuarm:~# cat /proc/sys/kernel/tainted
root@qemuarm:~# lsmod
Tainted: G
hello 846 0 - Live 0xbf000000 (O)

## Slide 32: Looking for module information (cont.)
and on the host system, using modinfo(8), which is not available on target due to it’s size limits
$ modinfo ~/kernel/modules/lecture1/3/hello.ko
filename: /home/serhii.popovych/kernel/modules/lecture1/3/hello.ko
license: Dual BSD/GPL
description: Hello, world in Linux Kernel Training
author: Serhii Popovych <serhii.popovych@globallogic.com>
depends:
vermagic: 4.9.20 preempt mod_unload ARMv5 p2v8
$ file ~/kernel/modules/lecture1/3/hello.ko
/home/serhii.popovych/kernel/modules/lecture1/3/hello.ko: ELF 32-bit LSB relocatable, ARM, version 1 (SYSV), BuildID[sha1]=3102ba3d1d1e837a2c059dff477cd3943378a227, not stripped

## Slide 33: Unloading your kernel module
It is very simple, just use rmmod(8) command line tool
root@qemuarm:~# rmmod hello

## Slide 34: Things to look in source code right now
Look at __init/__exit macro in <linux/init.h>
Look at module_init()/module_exit() macro implementation in <linux/module.h>
Look at MODULE_LICENSE() and comments about lincensing in <linux/module.h>
Explain EXPORT_SYMBOL() and EXPORT_SYMBOL_GPL() using any code component source (e.g. kernel/ or net/).
Explain module parameters support infrastructure using any drives/ source in-tree as example (e.g. drivers/net/ethernet/intel/igb)

## Slide 35: ANNEX

## Slide 36: General: prerequisites
BeagleBone Black board that already prepared as required in the previous homework
Working NFS boot path

## Slide 37: Make: entry for Linux Kernel maintenance
There is number of static analysis and report generation targets in makefile
Static analysers
checkstack - Generate a list of stack hogs
namespacecheck - Name space analysis on compiled kernel
versioncheck - Sanity check on version.h usage
includecheck - Check for duplicate included header files
export_report - List the usages of all exported symbols
headers_check - Sanity check on exported headers
headerdep - Detect inclusion cycles in headers
coccicheck - Check with Coccinelle.

## Slide 38: Make: entry for Linux Kernel maintenance (cont.)
There is also small set of useful targets to get information from the kernel tree using make for example from automation scripts.
Other targets, that might be useful are
$ make -s kernelversion
$ make -s kernelrelease
$ make -s image_name
modules_prepare - Set up for building external modules
headers_install - Install sanitised kernel headers to INSTALL_HDR_PATH
(default: ./usr)

## Slide 39: That’s all for now. Thank you for viewing.
Authors:
Serhii Popovych, Software Engineer
  Cisco-IOSXE Linux SDK, GlobalLogic Ukraine LLC
  Email: serhii.popovych@globallogic.com
Oleksandr Redchuk, Software Engineer
  GlobalLogic Ukraine
  Email: oleksandr.redchuk@gmail.com